SECTION 11 66 53.13

BATTING / GOLF CAGES

PART 1 – GENERAL

- SUMMARY

  - Section Includes

    - Ceiling Suspended Batting Cages.

      - BBC-700, 70' x 12' Single Pull Batting Cage.

      - BBC-7014, 70' x 14' Single Pull Batting Cage.

      - BBC-5512, 55' x 12' Single Pull Batting Cage.

      - BBC-5514, 55' x 14' Single Pull Batting Cage.

      - BBC-702, 70' x 12' Double Pull Batting Cage.

  - Related Sections

    - Section 05 00 00, Structural Metal Framing, Metal Joists.

    - Section 26 00 00, Electrical, Installing electrical power to operate gymnasium equipment.

- REFERENCES

- ASTM B221 - Standard Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Profiles, and Tubes.

- SUBMITTALS

- Comply with Section 01 33 00 – Submittal Procedures.

  - Certificates:  Submit manufacturer’s certificates for proof that all materials comply with specified requirements.

  - Design Data:  Submit manufacturer’s design data, including loads to be transmitted to building structural members with requirements of any additional structure needed.

  - Field Test Reporting:  Submit manufacturer’s certified destructive test reports completed by an accredited independent testing laboratory, indicating compliance with any specified factor or safety.

  - Shop Drawings:  Submit manufacturer’s shop drawings, including elevations, plans, sections, layouts, component locations, dimensions, tolerances, fabrication details, materials, finish, quantities, hardware, fittings, electrical wiring diagrams, additional structure needed details, and method of attachment.

  - Product Data:  Submit manufacturer’s product data, including proposed components, fabrication, finish, and materials.

  - Samples:  Submit manufacturer’s cage netting samples.

  - Installation, Operation, and Maintenance Instructions:  Submit installation, operation, and maintenance instructions including detailed step-by-step installation, troubleshooting, general operation instructions, and any recommended routine maintenance.

  - Warranty:  Submit manufacturer’s guarantees and warranty information on a system and/or component.

- QUALITY ASSURANCE

- Manufacturer Qualification:  All components to be provided from a single source manufacturer.

- Installer Qualification:  All components to be installed by a trained and qualified installer approved by the manufacturer.

- DELIVERY, STORAGE, AND HANDLING

- Delivery:  Deliver batting cage in original manufacturer’s containers, with all containers grouped together, with labels clearly labeling the manufacturer and contents.  Upon delivery, immediately inspect delivery for any missing containers or damage.  Any damage or defects shall be noted and reported to the Owner’s Representative.

- Storage:  Store containers in a clean, dry indoor location.

- Handling:  Protect materials and finish during handling and installation.

- Replacements:  If necessary, replacements shall be immediately re-ordered, so as to minimize any conflict with the construction schedule.

- WARRANTY

  - Batting cage system shall be guaranteed against defects in material and workmanship for a period of one (1) year.  Other components may be covered by their own extended warranty.

PART 2 – PRODUCTS

- MANUFACTURER

- Jaypro Sports, LLC. 976 Hartford Turnpike, Waterford, Connecticut 06385. Toll Free 800-243-0533. Phone 860-447-3001. Fax 800-988-3363. Email info@jaypro.com. Web www.jaypro.com.

- Manufactures of equivalent products will be considered in accordance with Section 01 25 13, Product Substitution Procedures.

- BATTING / GOLF CAGES

  - BBC-700, 70' x 12' Single Pull Batting Cage.

    - Size: 70' long x 12' wide x 11' high.

    - Operation:  Electrically operated cage moving up and down by cables wound onto overhead rotating drive pipe.

    - Drive System:  UL listed, 1 HP, 110VAC 60hz Single-phase compensating type instantly reversible winch, direct drive, self lubricated gearing, with built-in POSILOK™ over-speed arrest system, and integral limit switches to control cage travel.

    - Frame:  Constructed of 1.90" O.D. x 0.145" wall aluminum tube with cross supports spaced symmetrically along the length of the cage.  Frame assembled with galvanized malleable iron T and L fittings with case hardened setscrews.

    - Hoist Cables:  7 individual hoist lines placed symmetrically along cage and terminating at cage frame in 21 locations.  Cables shall be 1/8" diameter steel aircraft cable with 1,800 lb break strength.

    - Single hoist cable "clew" system shall not be approved as equal.

    - Drive Pipe:  2-3/8" outer diameter galvanized pipe supported by drive pipe carriers.

    - Storage:  Net thrown on top of cage for maximum overhead storage.

    - Control System:  Wall mounted, three-position momentary contact key switch with polished wall plate located so the operator has full view of cage during operation.

    - Attachment:  Rigidly suspended from building structure with heavy duty clamp style fittings.

<< << << SPECIFY ONE OF THE FOLLOWING PARAGRAPHS REGARDING THE CAGE NETTING SIZE.  BASEBALL 1-3/4" NETTING IS STANDARD. >> >> >>

    - Baseball Cage Netting:  1-3/4" Square #42 Black Nylon (STANDARD).  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

    - Multi-Sport Cage Netting:  3/4" Square #252 Black Nylon.  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

<< << << SPECIFY CUSTOM FEATURES BELOW >> >> >>

    - Optional Features:

      - ETEC Easy Touch Equipment Controller

      - MEC-99 MEC PAD Master Equipment Controller

      - DRX-1199 & TRX-1000 Wireless Remote Receiver and Transmitter

  - BBC-7014, 70' x 14' Single Pull Batting Cage.

    - Size: 70' long x 14' wide x 11' high.

    - Operation:  Electrically operated cage moving up and down by cables wound onto overhead rotating drive pipe.

    - Drive System:  UL listed, 1 HP, 110VAC 60hz Single-phase compensating type instantly reversible winch, direct drive, self lubricated gearing, with built-in POSILOK™ over-speed arrest system, and integral limit switches to control cage travel.

    - Frame:  Constructed of 1.90" O.D. x 0.145" wall aluminum tube with cross supports spaced symmetrically along the length of the cage.  Frame assembled with galvanized malleable iron T and L fittings with case hardened setscrews.

    - Hoist Cables:  7 individual hoist lines placed symmetrically along cage and terminating at cage frame in 21 locations.  Cables shall be 1/8" diameter steel aircraft cable with 1,800 lb break strength.

    - Single hoist cable "clew" system shall not be approved as equal.

    - Drive Pipe:  2-3/8" outer diameter galvanized pipe supported by drive pipe carriers.

    - Storage:  Net thrown on top of cage for maximum overhead storage.

    - Control System:  Wall mounted, three-position momentary contact key switch with polished wall plate located so the operator has full view of cage during operation.

    - Attachment:  Rigidly suspended from building structure with heavy duty clamp style fittings.

<< << << SPECIFY ONE OF THE FOLLOWING PARAGRAPHS REGARDING THE CAGE NETTING SIZE.  BASEBALL 1-3/4" NETTING IS STANDARD. >> >> >>

    - Baseball Cage Netting:  1-3/4" Square #42 Black Nylon (STANDARD).  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

    - Multi-Sport Cage Netting:  3/4" Square #252 Black Nylon.  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

<< << << SPECIFY CUSTOM FEATURES BELOW >> >> >>

    - Optional Features:

      - ETEC Easy Touch Equipment Controller

      - MEC-99 MEC PAD Master Equipment Controller

      - DRX-1199 & TRX-1000 Wireless Remote Receiver and Transmitter

  - BBC-5512, 55' x 12' Single Pull Batting Cage.

    - Size: 55' long x 12' wide x 11' high.

    - Operation:  Electrically operated cage moving up and down by cables wound onto overhead rotating drive pipe.

    - Drive System:  UL listed, 1 HP, 110VAC 60hz Single-phase compensating type instantly reversible winch, direct drive, self lubricated gearing, with built-in POSILOK™ over-speed arrest system, and integral limit switches to control cage travel.

    - Frame:  Constructed of 1.90" O.D. x 0.145" wall aluminum tube with cross supports spaced symmetrically along the length of the cage.  Frame assembled with galvanized malleable iron T and L fittings with case hardened setscrews.

    - Hoist Cables:  6 individual hoist lines placed symmetrically along cage and terminating at cage frame in 18 locations.  Cables shall be 1/8" diameter steel aircraft cable with 1,800 lb break strength.

    - Single hoist cable "clew" system shall not be approved as equal.

    - Drive Pipe:  2-3/8" outer diameter galvanized pipe supported by drive pipe carriers.

    - Storage:  Net thrown on top of cage for maximum overhead storage.

    - Control System:  Wall mounted, three-position momentary contact key switch with polished wall plate located so the operator has full view of cage during operation.

    - Attachment:  Rigidly suspended from building structure with heavy duty clamp style fittings.

<< << << SPECIFY ONE OF THE FOLLOWING PARAGRAPHS REGARDING THE CAGE NETTING SIZE.  BASEBALL 1-3/4" NETTING IS STANDARD. >> >> >>

    - Baseball Cage Netting:  1-3/4" Square #42 Black Nylon (STANDARD).  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

    - Multi-Sport Cage Netting:  3/4" Square #252 Black Nylon.  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

<< << << SPECIFY CUSTOM FEATURES BELOW >> >> >>

    - Optional Features:

  - ETEC Easy Touch Equipment Controller

  - MEC-99 MEC PAD Master Equipment Controller

  - DRX-1199 & TRX-1000 Wireless Remote Receiver and Transmitter

  - BBC-5514, 55' x 14' Single Pull Batting Cage.

    - Size: 55' long x 14' wide x 11' high.

    - Operation:  Electrically operated cage moving up and down by cables wound onto overhead rotating drive pipe.

    - Drive System:  UL listed, 1 HP, 110VAC 60hz Single-phase compensating type instantly reversible winch, direct drive, self lubricated gearing, with built-in POSILOK™ over-speed arrest system, and integral limit switches to control cage travel.

    - Frame:  Constructed of 1.90" O.D. x 0.145" wall aluminum tube with cross supports spaced symmetrically along the length of the cage.  Frame assembled with galvanized malleable iron T and L fittings with case hardened setscrews.

    - Hoist Cables:  6 individual hoist lines placed symmetrically along cage and terminating at cage frame in 18 locations.  Cables shall be 1/8" diameter steel aircraft cable with 1,800 lb break strength.

    - Single hoist cable "clew" system shall not be approved as equal.

    - Drive Pipe:  2-3/8" outer diameter galvanized pipe supported by drive pipe carriers.

    - Storage:  Net thrown on top of cage for maximum overhead storage.

    - Control System:  Wall mounted, three-position momentary contact key switch with polished wall plate located so the operator has full view of cage during operation.

    - Attachment:  Rigidly suspended from building structure with heavy duty clamp style fittings.

<< << << SPECIFY ONE OF THE FOLLOWING PARAGRAPHS REGARDING THE CAGE NETTING SIZE.  BASEBALL 1-3/4" NETTING IS STANDARD. >> >> >>

    - Baseball Cage Netting:  1-3/4" Square #42 Black Nylon (STANDARD).  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

    - Multi-Sport Cage Netting:  3/4" Square #252 Black Nylon.  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

<< << << SPECIFY CUSTOM FEATURES BELOW >> >> >>

    - Optional Features:

      - ETEC Easy Touch Equipment Controller

      - MEC-99 MEC PAD Master Equipment Controller

      - DRX-1199 & TRX-1000 Wireless Remote Receiver and Transmitter

  - BBC-702, 70' x 12' Double Pull Batting Cage.

    - Size: 70' long x 12' wide x 11' high.

    - Operation:  Electrically operated cage moving up and down by cables wound onto overhead rotating drive pipe.  Double pull hoist system allows for maximum clearance height beneath the frame in the stored position.  System stores approximately 2'-6" from existing structure.

    - Drive System:  UL listed, 1 HP, 110VAC 60hz Single-phase compensating type instantly reversible winch, direct drive, self lubricated gearing, with built-in POSILOK™ over-speed arrest system, and integral limit switches to control cage travel.

    - Frame:  Constructed of 1.90" O.D. x 0.145" wall aluminum tube with cross supports spaced symmetrically along the length of the cage.  Frame assembled with galvanized malleable iron T and L fittings with case hardened setscrews.

    - Hoist Cables:  14 individual hoist lines placed symmetrically along cage and terminating at cage frame in 14 locations.  Cables shall be 1/8" diameter steel aircraft cable with 1,800 lb break strength.

    - Single hoist cable "clew" system shall not be approved as equal.

    - Drive Pipe:  2-3/8" outer diameter galvanized pipe supported by drive pipe carriers.

    - Storage:  Net thrown on top of cage for maximum overhead storage.

    - Control System:  Wall mounted, three-position momentary contact key switch with polished wall plate located so the operator has full view of cage during operation.

    - Attachment:  Rigidly suspended from building structure with heavy duty clamp style fittings.

<< << << SPECIFY ONE OF THE FOLLOWING PARAGRAPHS REGARDING THE CAGE NETTING SIZE.  BASEBALL 1-3/4" NETTING IS STANDARD. >> >> >>

    - Baseball Cage Netting:  1-3/4" Square #42 Black Nylon (STANDARD).  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

    - Multi-Sport Cage Netting:  3/4" Square #252 Black Nylon.  All perimeters of the cage shall be sewn together bound to a 3/8" polypropylene rope.  Approximately 12" of netting shall lay on the floor when cage is in lowered position.

<< << << SPECIFY CUSTOM FEATURES BELOW >> >> >>

    - Optional Features:

      - ETEC Easy Touch Equipment Controller

      - MEC-99 MEC PAD Master Equipment Controller

      - DRX-1199 & TRX-1000 Wireless Remote Receiver and Transmitter

PART 3 – EXECUTION

- EXAMINATION

  - Examine areas of installation for any conditions that would affect the installation of the gymnasium equipment.  If conditions exist that prohibits or hinders installation, notify the Architect and do not proceed with the installation until conditions have been resolved.

- INSTALLATION

  - Install equipment in accordance with manufacturer’s instructions.

  - Install equipment level, straight, accurate in accordance with the supplied drawings and at the correct locations specified.

  - Install equipment with supplied hardware, fittings, and components.

  - Take care to keep gymnasium equipment clean during install and not damage equipment or finish.  Touch up finish if necessary.

  - For electrically operated equipment, install electrical power in accordance with Section 26, Electrical.

  - For electrically operated equipment, install control system such that the operation of the equipment can been seen in clear sight.

- ADJUSTING

- Adjust gymnasium equipment as needed to function properly and to ensure accurate position in both stored and in-use positions.

- For electric powered gymnasium equipment, adjust upper and lower limit switches as needed to achieve desired heights.

- CLEANING

- Clean gymnasium equipment in accordance with manufacturer’s instructions.

- Do not use harsh cleaning methods or supplies that may alter the finish of the gymnasium equipment.

- DEMONSTRATION

- Demonstrate complete operation of the gymnasium equipment to the Owner Representative.

- Furnish Owner Representative of operation procedure and required maintenance.

- Furnish Owner Representative with means necessary to operate gymnasium equipment.

- PROTECTION

- For installations of gymnasium equipment with finished floor already installed, provide means of protecting the floor to prevent damage.

END OF SECTION